## Slide 1: Turbidity Test of Water
By
Devansh Wadhwani – (64)
Diksha Utekar – (63)
D15A INFT

## Slide 2: Project Objective
Arduino-based system to measure water turbidity.
Uses a turbidity sensor to display real-time readings.
Useful for environmental monitoring and water quality.

## Slide 3: Components Used
Arduino UNO R3
Turbidity Sensor (SEN0189)
16x2 LCD Display (with I2C)
Jumper Wires
USB Cable

## Slide 4
Technical specifications of Components
Arduino UNO | Turbidity Sensor (SEN0189) | 16x2 LCD Display (I2C) | Jumper Wires | USB Cable
5V operating voltage 14 digital I/O pins, 6 analog inputs 16 MHz clock speed 32 KB flash memory | 5V supply voltage 0–1000 NTU measurement range Analog output signal Waterproof sensor head | 5V operating voltage 16 characters × 2 lines I2C communication (only 2 pins) Adjustable contrast | For quick connections Male/Male, Male/Female, Female/Female | USB A to B type Used for programming and powering Arduino

## Slide 5: Pin Connections - Turbidity Sensor
VCC to 5V
GND to GND
Signal to A0

## Slide 6
Turbidity Sensor Connection

## Slide 7: Pin Connections - LCD (I2C)
VCC to 5V
GND to GND
SDA to A4
SCL to A5

## Slide 8
LCD CONNECTIONS WITH ARDUINO

## Slide 9: Circuit Diagram

## Slide 10
Schematic Diagram

## Slide 11: Procedure - TinkerCAD Simulation
Simulate Arduino UNO and verify LCD.
Connect turbidity sensor.
Run sample codes.
Display Turbidity on LCD.

## Slide 12: Procedure - Physical Implementation
Connect LCD and turbidity sensor.
Upload and run code.
Test with various water samples.
Monitor LCD for turbidity readings.

## Slide 13: Arduino Code (Part 1)

## Slide 14: Arduino Code (Part 2)

## Slide 15: Explanation of Code
Initializes and sets up the LCD.
Reads sensor's analog values.
Judges the Purity of Water Sample
Displays turbidity readings on LCD.

## Slide 16: Applications
River and lake pollution monitoring
Industrial wastewater analysis
Aquaculture
Drinking water quality testing

## Slide 17: Conclusion
Learned sensor integration with Arduino.
Displayed and interpreted turbidity levels.
Built a practical environmental tool.